## Slide 1: What’s a bootloader and why its needed ??
Bootloader :
Bootloader is nothing but a small piece of code stored in the MCU flash or ROM to act as an application loader as well as a mechanism to update the applications whenever required.

## Slide 2
ATmega328P
Does this MCU come with on chip Bootloader ?
Yes it is !
Does it run whenever MCU undergoes reset ?
Yes. Upon reset, Arduino bootloader runs first
What’s the main use of bootloader ?
To Download Arduino sketches to the board.(IAP)

## Slide 3
STM32f446RE
Does this MCU come with on chip Bootloader ?
Yes it is !
Does it run whenever MCU undergoes reset ?
No. Should activate changing the status of boot pins
What's the main use of bootloader ?
To Download/Upload binaries (IAP)
STM32f446RE Nucleo 64

## Slide 4
TM4C123G
Does this MCU come with on chip Bootloader ?
Yes. TivaWare Bootloader
Does it run whenever MCU undergoes reset ?
No. Should activate changing the status of boot pins
What's the main use of bootloader ?
To Download/Upload binaries (IAP)
TM4C123G LaunchPad

## Slide 7: STM32F446XX Memory Organization
Internal Flash memory also called as Embedded Flash memory of 512KB
Internal SRAM1 of 112KB
Internal SRAM2 of 16KB
System Memory (ROM) of 30KB
OTP memory of 528 bytes
Option bytes memory of 16bytes.
Backup RAM of 4KB

## Slide 8: Internal Flash memory
Size is 512KB
Begins @ 0x0800 0000
Ends @ 0x0807 FFFF
Used to store your application code and read only data of the program
Non volatile

## Slide 9: Internal SRAM1
Size is 112KB
Begins @ 0x2000_0000
Ends @ 0x2001_BFFF
Used to store your application global data, static variables
Also used for Stack and Heap Purpose
Volatile
You can also execute code from this memory

## Slide 10: Internal SRAM2
Size is 16KB
Begins @ 0x2001_C000
Ends @ 0x2001_FFFF
Used to store your application global data, static variables
Also can be used for Stack and Heap Purpose
Volatile
You can also execute code from this memory

## Slide 11
All ARM Cortex M Based MCUs right after reset does,
Load value @ Memory addr. 0x0000_0000 in to MSP
Load value @ Memory addr. 0x0000_0004 in to PC (Value = Addr of the reset handler)
In STM32 Microcontroller ,
MSP value stored at 0x0800_0000
Vector table starts from 0x0800_0004
Address of the reset handler found at 0x0800_0004
So , Don’t you think we should somehow link 0x0800_0000 to 0x0000_0000 ??

## Slide 12
Processor Memory Map
0x0000_0000
0x0000_0004
0x0000_0008
0x0000_000C
0x0800_0000
0x0800_0004
0x0800_0008
Our User flash begins here
MSP
Reset Hndlr Adr.
Memory Aliasing
After reset Processor looks here
(Depends on MCU)
Notes: Depends on MCU

## Slide 13: System Memory ( ROM)
Size is 30KB
Begins @ 0x1FFF_0000
Ends @ 0x1FFF_77FF
All the ST MCUs store Bootloader in this memory
This Memory is Read only
By default MCU will not execute any code from this memory but you can configure MCU to boot or execute bootloader from this memory .

## Slide 14: Boot Configuration of STM32F446xx

## Slide 15
Bootloader : Code Placement in Flash
ST Bootloader
ROM (30KB)
Sector 0 (16KB)
Sector 1 (16KB)
Our Bootloader
Sector-2 to Sector-7 will be used for storing user application

## Slide 16
Host – Bootloader Communication
ACK/NACK + Length to follow
(2bytes)
Reply ( of “length to follow” bytes)
HOST
MCU
(Bootloader)
Command Packet

## Slide 17
Bootloader
USART2
USART3
From PC
Virtual COM Port
Debug port
To PC
To PC
STM32

## Slide 18
Length
to follow
Command
Code
CRC
1
1
4
Total Bytes of the packet = 6
“Length to follow ” field will contain the value : 5
Command Code : 0x51
Boot loader version number
(1 byte)
Bootloader reply
Bootloader command
Command Name : BL_GET_VER

## Slide 19
Length
to follow
Command
Code
CRC
1
1
4
Total Bytes of the packet = 6
“Length to follow ” field will contain the value : 5
Command Code : 0x52
Supported Commands codes
Bootloader reply
Bootloader command
Command Name : BL_GET_HELP

## Slide 20
1
Length
to follow
Command
Code
CRC
1
4
Total Bytes of the packet = 6
“Length to follow ” field will contain the value : 5
Command Code : 0x53
(2 bytes)
MCU chip Id
LSB
MCU chip Id
MSB
Command Name : BL_GET_CID
Bootloader reply
Bootloader command

## Slide 21
Length
to follow
Command
Code
CRC
1
1
4
Total Bytes of the packet = 6
“Length to follow ” field will contain the value : 5
Command Code : 0x54
(1 bytes)
RDP status
Command Name : BL_GET_RDP_STATUS
Bootloader reply
Bootloader command

## Slide 22
(1 byte)
status
Length
to follow
Command
Code
CRC
1
1
4
Memory address
(LE)
4
Total Bytes of the packet = 10
“Length to follow ” field will contain the value : 9
Command Code : 0x55
Command Name : BL_GO_TO_ADDR
Bootloader reply
Bootloader command
Base Memory Addr. :
4 Byte base address to jump

## Slide 23
(1 byte)
status
Length
to follow
Command
Code
CRC
1
1
4
Sector
Number
1
Number
of sectors
1
Total Bytes of the packet = 8
“Length to follow ” field will contain the value : 7
Command Code : 0x56
Command Name : BL_FLASH_ERASE
Bootloader reply
Bootloader command
Sector number : 0 , 1 , 2 , 3 , 4 ,5 , 6 ,7
Number of sectors : 0 to 7

## Slide 24
(1 byte)
status
Length
to follow
Command
Code
payload
1
1
X
Base Memory address
(LE)
4
Payload
Length(X)
CRC
1
4
Total Bytes of the packet = 11+X
“Length to follow ” field will contain the value : 10+X
Command Code : 0x57
Command Name : BL_MEM_WRITE
Bootloader reply
Bootloader command
Base Memory Addr. :
4 Byte base address
Payload len: No. of bytes to write
Payload : bytes to write

## Slide 25
(1+”len” bytes )
Length
to follow
Command
Code
CRC
1
1
4
Base Memory addr.
(LE)
4
len
1
Total Bytes of the packet = 11
“Length to follow ” field will contain the value : 10
Command Code : 0x59
Command Name : BL_MEM_READ
Bootloader reply
Bootloader command
status
“len” number of bytes
Base Memory Addr. :
4 Byte base address from which data has to be read
len : No. of bytes to read

## Slide 26
Length
to follow
Command
Code
CRC
1
1
4
(2 bytes)
All Sectors status
Total Bytes of the packet = 6
“Length to follow ” field will contain the value : 5
Command Code : 0x5A
Command Name : BL_READ_SECTOR_STATUS
Bootloader reply
Bootloader command

## Slide 27
(1 bytes)
status
Length
to follow
Command
Code
CRC
1
1
4
1
Sector
Details
1
Protection
Mode
Total Bytes of the packet = 8
“Length to follow ” field will contain the value : 7
Command Code : 0x58
Command Name : BL_EN_R_W_PROTECT
Bootloader reply
Bootloader command
Sector details : sector numbers encoded in 8bits (ex: 0th bit is sector 0)
1: protection
0: No protection
Protection Mode :
1(Write Protection )
2 (R/W protection)
Notes: Sector number : 0 , 1 , 2 , 3 , 4 ,5 , 6 ,7
Operation Code : 0(No Protection) , 1(Write Protection ) , 2 (R/W protection)

## Slide 28
(1 bytes)
status
Length
to follow
Command
Code
CRC
1
1
4
Total Bytes of the packet = 6
“Length to follow ” field will contain the value : 5
Command Code : 0x5C
Command Name : BL_DIS_R_W_PROTECT
Bootloader reply
Bootloader command
Disables Active protection on all the sectors (resumes to default state)

## Slide 29
Reset of MCU
Inits:
HAL
GPIO
UARTx
CRC
Clock
User Button pressed?
bootloader_uart_read_data()
bootloader_jump_to_user_app()
Y
N
Bootloader Code Flow Chart

## Slide 30
bootloader_uart_read_data()
Poll UART for data
Length byte received ?
Read “length” number of bytes
Decode command
Handle_X_command
Finish Handle_X_command
Y
N

## Slide 31
Handle_X_command
Good CRC?
Send “NACK”
Send “ACK”
Obtain reply
Send reply
Finish : Handle_X_command
bootloader_uart_read_data()
N
Y